## Slide 1: 4.2: Metadata / Task Team Report
Henry Kleta, acting Chair of Metadata Task Team

## Slide 2: Metadata
SOT Task Team on metadata, membership:
Chair: Emma Steventon (seconded till end of year to another position)
Acting chair: Henry Kleta
Vice chair: vacant
Martin Kramp Anthonin Lize
Jean-Baptiste Cohuet David Berry (leaving)
Joel Cabrie Eric Freeman
Venkat Shesu Reddem Matthias Hoigt
Rudolf Krockauer Rebecca Cowley
Tamaryn Morris Richard Cornes
Puneet Jaswal

## Slide 3: Metadata
SOT Task Team on metadata, Terms of References (suggestion, based on ToRs of pre-SOT-10 metadata TTs – VOS and SOOP had one...) :
Develop a new composite metadata structure for SOT observing networks based upon new WIGOS metadata standards and existing WMO Pub No 47 metadata requirements.
Regularly review metadata requirements for SOT observing networks and propose amendments or recommendations where considered appropriate.
Review the compliance of SOT networks with WIGOS requirements. Liaise with OSCAR Working Groups where required.
Monitor related work undertaken by other GOOS observing networks to ensure that, where appropriate, consistent harmonised metadata provisions are developed.
Liaise with the Task Team on Recruitment, Promotion and Training concerning metadata training for VOS operators, Focal Points and PMOs.
Determine the minimum SOT metadata requirements to be aligned with OSCAR mandatory metadata.

## Slide 4: Metadata
Activities of Metadata Task Team in intersessional period:
Various meetings and regular Tele-Conferences were and are still held
VOSP Chair spent September 2020 at OceanOPS for dedicated work on future SOT metadata format
Reference tables were defined to standardize data as much as possible, most tables are finalized
New format presented to SOT-EB, agreement received
Discussion with OceanOPS concerning implementation in progress
Definition of Test cases and scenarios
Final adjustments in progress

## Slide 5: Metadata
Pub47
VOS only metadata format , fully ship focused
SOT metadata format
metadata format for VOS, SOOP and ASAP stations
format is compatible with WIGOS / OSCAR requirements
history of metadata will be available
OceanOPS will act as metadata repository
WIGOS / OSCAR input from OceanOPS on behalf of operators
SOT metadata format:
  one block for ship metadata
  one block for station metadata
  one block for sensor metadata
  one ship can host one or more stations
  one station can have one or more sensors connected to it

## Slide 6: Metadata
Mandatory fields to request an SOT-ID
Name of Ship
IMO-number or ICES-code (if neither is available, OceanOPS will help)
Hide Ship Metadata Option (Yes/No), must be confirmed by SHIP-TC
GTS-ID (ID of realtime datastream in GTS, SOT-ID recommended)
Class-Category (VOS: VOS class, all other: NIL)
Programme (autogenerated based on operator)
Additional Mandatory fields to register station in OceanOPS database
Schedule of Observation
Installation date
Information on station (make, model, data transmission)
Information on sensors (parameter, make, model, installation date)

## Slide 7: Metadata
Ship metadata
Name | M / O / C | Content of field | Remark | Example
Ship Name | M² | free text |  | Sonne
IMO# | M² | 9 digits (ready for extension) | if available, else NIL | 9633927
ICES code | M² | 4 char | if available, else NIL | NIL
Country of registration | C | ISO 2 | Flagstate of vessel | DE
Call Sign | C | min 4 max 7 char |  | DBBE
MMSI |  |  |  | 21162740
Hide Ship Metadata Option | M² | boolean | 1 (Yes) / 0 (No) | 0
Vessel type | C | ref table |  | RV
vessel length | C | real, . decimal meters |  | 118.42
vessel breadth | C | real, . decimal meters |  | 20.6
freeboard | C | real, . decimal meters |  | NIL
draft | C | real, . decimal meters |  | 6.4
cargo height | C | real, . decimal meters |  | NIL
distance bridge bow | C | real, . decimal meters |  | NIL
max speed | C | real, . decimal knots |  | 15.0
Shipping Company | O | free text |  | Briese
Ship Contact Shore Name | O | free text | e.g. shipping company | Briese Research
Ship Contact Shore eMail | O | eMail address | eMail address of PIC | not public
Ship Contact Sea eMail | O | eMail address | eMail adddress of ship | not public

## Slide 8: Metadata
Station metadata
Name | M / O / C | Content of field | Remark | Example
GTS-ID | M² | min 4 max 7 char | call sign, MASK, SOT-ID | BLSFV3U
Class-Category | M² | ref table | VOS: new VOS class | NMHS operated
Programme | M² | ref table | based on operator | VOS-DE
Additional Programme Affiliation | O | ref table |  | E-SURFMAR
Schedule of Observation | M | ref table |  | hourly
Area of Operation | O | ref table | e.g. target XBT line | NIL
Target Inspection Interval | O | ref table |  | annual
start date | M | YYYY-MM-DD | installation date | 2014-02-10
stop date | O | YYYY-MM-DD |  | NIL
Observing Height | O | real, . decimal meters | visual observing height | 14.0
Observing system main device | M/O | ref table | e.g. AWS or XBT Recorder | EUCAWS
main device serial number | O | ref table |  | 00367462
main device version number | O | ref table |  | 0.4.2
Observing system ancillary device | M/O | ref table | e.g. TBW or XBT Launcher | TurboWin
ancillary device serial number | O | ref table |  | NIL
ancillary device version number | O | ref table |  | 5.0
Maintenance activity | O |  |  | NIL
Telecom Service | M | ref table |  | ISDB
Telecom Type | O | ref table | can be unknown | Iridium
Latency | M | ref table |  | less than 1 hour
Ship2Shore dataformat | M | ref table |  | #100

## Slide 9: Metadata
Sensor metadata
Name | M / O / C | Content of field | Remark | Example
parameter:make_model | M:M | ref table:ref table | ID ref table | ATM:Vaisala_PTB
serial | O | serial number of sensor |  | 1234
start date | M | YYYY-MM-DD |  | 2020-04-29
stop date | O | YYYY-MM-DD |  | NIL
configuration | O | ref table |  | vented
configuration - location | O | ref table |  | Technical room
configuration - sideindicator | O | ref table | STB;PB,NIL | NIL
measurement unit | O | autogenerate or overwrite |  | NIL
vertical distance from SLL | O | real, . decimal meters |  | 14.0
height of sensor above deck | O | real, . decimal meters |  | 1.8
distance from bow | O | real, . decimal meters |  | NIL
distance from center line | O | real, . decimal meters |  | NIL
date of last calibration | O | YYYY-MM-DD |  | 2021-05-01
next calibration due date | O | YYYY-MM-DD |  | 2023-05-01
instrument operating status | O | autogenerate |  | NIL
instrument specs: range | O | autogenerate or overwrite |  | NIL
instrument specs: resolution | O | autogenerate or overwrite |  | NIL
instrument specs: precision | O | autogenerate or overwrite |  | NIL
instrument specs: accuracy | O | autogenerate or overwrite |  | NIL
sensor sampling period | O | ref table | sensor specific | 9sec
total sampling period | O | ref table | observation specific | 1min
data processing algorithms | O | ref table |  | mean
instrument control schedule | O | ref table |  | annually

## Slide 10: Metadata
Plan forward...
OceanOPS will implement new website / frontend to allow easy entry of stations using new metadata format
Operators will be able to receive Pub47 metadata and map the according fields into the new metadata format for an interim period (suggest till SOT-12)
OceanOPS will be able to provide Pub47 sets to data users such as archives for an interim period (suggest: till SOT-12)
Action: Metadata providers and users are requested to adapt their dataflows to the new SOT metadata format (Operators, data archives, etc: SOT-12).

## Slide 11: Metadata
Actions (from SOT-10)
Ref. Item | Action Item | By | Deadline | Update
A6.6/1 | The new composite metadata document should continue to be drafted for SOT networks, based on WIGOS requirements and with the view to eventually replace WMO Pub-47. | TT-Metadata | May 2020 | final adjustments in progress
A6.6/2 | Following the Task Team review of WIGOS Pub-1160, new code tables need to be developed for the composite format to capture metadata required for VOS operational activities (but that are not required by WIGOS) | TT-Metadata | SOT-11(ongoing) | final adjustments in progress
A6.3/3 | Proposed new composite metadata format be adopted once competed, agreeing the proposed phased approach for VOS | TT-Metadata | SOT-11(ongoing) | General acceptance from SOT-EB received
A6.3/4 | VOS operating members and PMOs should be invited to review both the proposed new composite metadata format and the visual JCOMMOPS display and to notify the Task Team if they identify any gaps or consider that further amendments are required. | TT-VOS Metadata, VOS Operators / PMOs, JCOMMOPS | SOT-11(ongoing) | pending
A6.3/5 | Training for VOS Operators and Port Met Officers in the collection and management of metadata should be considered in liaison with the Task Team on Recruitment, Promotion & Training (TT-RPT) | TT-RPT & TT-Metadata | SOT-11(ongoing) | pending

## Slide 12: Metadata
Actions (from SOT-10) - continued
Ref. Item | Action Item | By | Deadline | Update
A6.7/1 | Chairs of TT-VOS Metadata and TT-SOOP Metadata to review the ToR of TT-Metadata (VOS SOOP Metadata combined TT) and send it to SOT EB for review and approval | Chairs of TT-VOS Metadata & TT-SOOP Metadata | May 2019 | done
A6.7/2 | Work with the SOT Technical coordinator on the definition and consolidation of new TSG/pCO2-specific metadata fields. This effort should include the development of a BUFR template to support TSG/pCO2 operations. | TT- Metadata &SOT-TC, David Berry | SOT-11 | final adjustments in progress
A6.7/3 | Assess and report the convenience of upgrading TM315004 to accommodate additional metadata requirements. | TT- Metadata &SOT-TC , David Berry | SOT-11 | ?
A13.4/1 | Develop documentation on how/what to migrate from PUB47 to JCOMMOPS metadata database. | TT-Metadata | SOT-11 | pending

## Slide 13: Discussion