## Slide 1
Funded by NOAA Global Ocean Monitoring and Observing Program (GOMO)
Partnership of 5 institutions:
  NOAA/AOML
  NOAA/PMEL
  NOAA/GML
  Univ. of Miami/RSMAS (academic partner)
  BIOS (Bermuda)(academic partner)
Goal: To constrain the flux of CO2 across the air-water interface to within 20% on regional and seasonal scales to provide meaningful projections of future atmospheric CO2 levels, and surface oceanic CO2 concentrations
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
Sea-air CO2 flux = k Ko ∆pCO2
Notes: Sea-air CO2 flux = k Ko ∆pCO2 : the sea-air CO2 flux is determined from the gas transfer velocity (k), the solubility of CO2 (Ko) and the partial pressure difference between the surface ocean and atmosphere. The ocean carbon program sponsored by NOAA CPO/COD supports the largest sustained measurement campaign from ships of opportunity in the world contributing roughly half of all the data that goes into the SOCAT effort (Surface Ocean Carbon ATlas) that is used as a comprehensive database to constrain the amount of CO2 entering the ocean.

## Slide 2
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
Largest ship of opportunity pCO2 measurement campaign in the world
Comprised of 15 ships of opportunity with automated CO2 systems in FY20
Research vessels, Cargo ships, Cruise ships
Ship tracks and ships with autonomous pCO2 systems sponsored by the NOAA/GOMO program in FY 2017-2020
Notes: Sea-air CO2 flux = k Ko ∆pCO2 : the sea-air CO2 flux is determined from the gas transfer velocity (k), the solubility of CO2 (Ko) and the partial pressure difference between the surface ocean and atmosphere. The ocean carbon program sponsored by NOAA CPO/COD supports the largest sustained measurement campaign from ships of opportunity in the world contributing roughly half of all the data that goes into the SOCAT effort (Surface Ocean Carbon ATlas) that is used as a comprehensive database to constrain the amount of CO2 entering the ocean.

## Slide 3
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes

## Slide 4
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
2019
2020
Inconsistent coverage of major oceans from year to year.
Pandemic. 2019: 760k data points 2020: 360k data points

## Slide 5
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
New CO2 analyzer – old one discontinued
high-precision, high-stability, laser-based gas analyzer that uses Optical Feedback — Cavity-Enhanced Absorption Spectroscopy (OF-CEAS) to measure gases in air.
Improvements: less gas standards, less frequent calibrations, better handle on water interference
Hurdles: Different form factor, gas flow rate required re-design of our system.
New system should be on the market very soon.
Re-design of the underway system

## Slide 6
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
System has increased failures in hot environment.
  Use engine room ventilation in cold weather
Data losses due to lack of access to ships
Data losses due to lack of support on ship
SHIP RECRUITMENT
Issues of the program

## Slide 7
SOOP-CO2
Ocean Carbon Cycle – Sea-air CO2 fluxes
Groundtruthing of alternate sensors, unmanned vehicles, remote sensors, models
Need to improve the constraint of the CO2 flux in the global carbon cycle to better our understanding and predictions of the system.
Need to improve measurements, temporal and spatial coverage to assess carbon dioxide removal (CDR) techniques.
Future of the program – increased importance
Thank you