## Slide 1
Colombian Oceanographic and Marine Meteorological Network
RedMpomm Red de Medición de Parámetros Oceanográficos y de Meteorología Marina REDMPOMM

## Slide 2: Red de Medición de parámetros Oceanográficos y de meteorología marina RedMpomm
Is a network that allows for real-time meteo-marine data from the Colombian Caribbean and Pacific Seas.
This monitoring network allows the observation of real-time data related to oceanic and atmospheric conditions of the "Colombian maritime territory", in order to provide information necessary to guarantee and safeguard human life in the various maritime and coastal activities carried out in the country.
It is interconnected with weather stations, directional wave buoys and Metereo-oceanic buoys located in different national maritime points near major ports and coastal cities,
Which record data such as speed and direction of wind, temperature, relative humidity, atmospheric pressure, Sun radiation and sea state: direction and speed of currents up to 50 meters; period, height and wave direction, sea surface temperature, surface salinity
DIMAR - RedMpomm is a network created for safety and maritime security, monitoring tsunami and Marine Meteorological events
General Maritime Directorate - Dimar is responsible for operating and maintaining the Sea Level data

## Slide 3: Ubication And Data Transmission Station tide Gauge
Malpelo
Tumaco
B. Solano
Buenaventura
B. Málaga
Juanchaco
Turbo
Providencia
San Andres
Ballenas
P. Bolívar
P. Estrella
P. Brisa
Santa Marta
Barranquilla
I. Naval
Cartagena
Coveñas
I. Fuerte
Sapzurro
P. Espada
Candelilla
Data Transmission
Systems
Principal: GPRS / Movil
Secondary: Satelital GOES, BGAN Inmarsat
Protocol
HTTP - Remote management
FTP
remote areas- does not have good mobile coverage

## Slide 4: Configuration a sensors
Sensors
Datalogger: OTT NetDL1000
Principal sensor
Radar level sensor (RLS -OTT Hydromet)
Secondary Sensor
bubbler sensor for surface water level monitoring (CBS-OTT Hydromet)
Measurement unit: Meters
Transmission Format: OTT Binary, *.mis
Solar panel
Antenna GOES/GPRS/BGAN
Datalogger
Batt
Radar sensor
Bubbler
Sensor
*Pressure sensors not conditioned for local area

## Slide 5: Configuration a sensors
Bahía Solano
Juanchaco
Bahía Málaga

## Slide 6: Configuration a sensors
Malpelo

## Slide 7: Configuration a sensors
Coveñas

## Slide 8: Data management
Quality control Handbook for Tide Gauge
Data standardization – IODE – The Colombian Oceanographic Data Center (Cecoldo)
Data Update: 6-12 months
DATA BASES
Hydras Ftp/Goes
Hydras HTTP
SQL primary
Sql standardized
standardized

## Slide 9: Data management
Hydras Ftp/Goes
Hydras HTTP
SQL SERVER Primary
SQL SERVER
standardized
Cecoldo
Real Time data
Update 2/5 min
Update 6 month
Update 12 month

## Slide 10: IOC data sharing Status
FTP 30 min

## Slide 11: IOC data sharing Status
Coveñas

## Slide 12: IOC data sharing Status

## Slide 13: IOC data sharing Status
Thank you for your attention
walvarez@dimar.mil.co