## Slide 1
Getting data into the IOC-SLSMF
SEA LEVEL STATION MONITORING FACILITY
Bart Vanhoorne, Francisco Hernandez
Flanders Marine Institute (VLIZ)
Belgium
www.ioc-sealevelmonitoring.org

## Slide 2: From tide gauge to the facility by GTS, HTTP push, FTP, webservice, email, socket
GTS
Database
Belgian
MetOffice
HTTP push
FTP / webservice / email / socket
6 methods

## Slide 3: Method 1 – GTS
Global Telecommunication System
Managed by WMO
Weather data/earth observations between nodes
Combination of satellite, land lines, internet, ...

## Slide 4: Method 1 – GTS How is data transferred?
Measurements generated by sensor
Grouped into a message by logger, at station
Logger sends message to satellite via modem, incl. unique Data Collection Platform (DCP) address, DCP_ID
Messages collected by satellite operators (METEOSAT, GOES, ...)
Message put and routed on the GTS network to configured destinations

## Slide 5: Method 1 – GTS Message arrival & parsing at VLIZ
GTS -> Royal Meteorological Institute of Belgium (RMI) -> VLIZ FTP subset of all GTS: filtered by WMO header
100+ messages from last minute from all stations uploaded in one file.
PHP script:
  downloads files 1x/min (pull)
  each station: metadata entry with DCP_ID (see later)
  loop through all GTS stations, when DCP_ID match: use parsing parameters (sensor, start, end, unit)
  insert into database: (sensor, timestamp, sealevel measurement) – value “AS IS”
  Multiple message formats ASCII, CREXX, pseudo binary, ...

## Slide 6: Method 1 – GTS Message parsing example: ASCII

## Slide 7: Method 1 – GTS Message parsing example: binary/GOES

## Slide 8: Method 2 – FTP How is data transferred?
Measurements generated by sensor
Script on logger or server groups & transforms it to format similar as <timestamp><separator><value>
File uploaded to own server or VLIZ FTP
Files named consistently, but organized in many different ways: by station name, sensor, date, ...
Two methods: same file constantly updated <-> new file for each (batch of) measurements

## Slide 9: Method 2 – FTP Script processing at VLIZ
Config in in PHP script: server & path, format, station code
Downloads files 1x/5min/each FTP (pull)
Each provider != format & file/folder structure => custom parsing function per provider
Metadata (code, sensor) retrieved from DB, based on config
Specific parser for provider generates: <station><sensor><timestamp><measurement>
Insert into database “AS-IS”

## Slide 10: Method 2 – FTP File organisation example
1 file per day, updated 1x/5min (i.e. Korea)
1 file forever (i.e. Colombia)
New file each 5min (i.e. SHOM)

## Slide 11: Method 2 – FTP File parsing example
Data file
PHP config: server, login, pass, path
Custom parsing function (i.e. SHOM)

## Slide 12: Method 3 – Email Processing script at VLIZ
Providers sends (scripted) email that contains sensor measurements
PHP script reads emails from mailbox gauges@vliz.be, 1x/3min (pull)
Config in script: subject, sender, station code
Rest of the processing => same as FTP
Not used any longer

## Slide 13: Method 4 – webservice (or “HTTP pull”)
Providers sets up webservice that returns sensor measurements when sending a HTTP request (~browser)
Examples http://tidesandcurrents.noaa.gov, SHOA, ...
Script reads 1x/3min/each webservice URL (pull)
Configuration in in PHP script: URL, format, station code
Rest of the processing => same as FTP

## Slide 14: Method 4 – webservice Parsing example
Webservice URL https://niveldelmar.snam.cl/apps/src/ws/wsgateway.php ?wsname=getData &idcanal=gprs &period=12 &date=2022-09-26T13:00:00 &idestacion=valp

## Slide 15: Method 5 – HTTP push (or referred to as “BGAN”)
Station is connected to the public internet via 4G, GPRS, satellite, ...
Script on logger sends HTTP POST request to the SLSMF webserver, containing measurements from sensor
Webserver processes posted messages via same method & data format as GTS
Measurements immediately added to the database: 0 delay (push)
Whitelist of IP addresses that can push

## Slide 16: Method 5 – HTTP push Example
Manual http://www.ioc-sealevelmonitoring.org/bgan/
Message parsing => identical as GTS

## Slide 17: Method 6 – TCP Socket
Station is connected to the public internet via 4G, GPRS, satellite, ...
Logger (or server at provider) opens TCP port that streams measurements from sensor in real time (i.e. 1/sec)
Config in in PHP script: TCP address, format & station code
PHP script connects to TCP port, reads measurements & immediately added to the database = 0 delay (~push)

## Slide 18: Method 6 – TCP Socket Example
Config in PHP script
Measurements streamed at the bottom
Message parsing => identical as FTP/webservice: custom function
measurements

## Slide 19
Method comparison
 | GTS | FTP | Email | HTTP push | Webservice | Socket
Transmit interval (min) | 5 ..15 | 1 .. 60 | 1 .. 60 | 1 .. 15 | 1 .. 6 | 0.01 .. 1
# stations | 556 | 216 | 0 | 60 | 334 | 5
Typical delay (min) | 2 .. 15 | 3 .. 60 | 3 .. 60 | 0 ..15 | 1 .. 6 | 0 .. 1
Ratio expected/ arrived (%) | ~100% | < 90% | < 90% | ~100% | < 95% | < 100%
Data format standard | some | none | good | good | good | good
Mechanism for VLIZ | pull | pull | pull | push | pull | push
Access | Restricted (WMO) | Easy | Easy | Transmission expensive | Set up server & API | Set up server
Issues | Format decoding sometimes hard | Many formats, many file structures. Quite some communication errors | No longer used | Many station non-functional. | Many formats. Quite some communication errors | Not much used. Some communication errors

## Slide 20: Edit metadata
Edit most station metadata
Add/edit sensors
Add/edit GTS parsing parameters
< method

## Slide 21: Survey results summary
 | Ecuador | Peru | Colombia
Stations in SLMF | 3 GTS | 3 GTS | 8 GTS 6 FTP
Operational | 3 GTS | 2 GTS | 6 GTS
Additional stations | 11 | 17 | 2
Telemetry | webservice | GPRS/INMARSAT | GOES/BGAN

## Slide 22: Stations provided by Instituto Oceanográfico de la Armada (Ecuador) Status at 2022-09-25: 3 stations listed
Code | Country | Location | Connection | DCP ID | Delay | Transmit Interval
balt | Ecuador | Baltra,Galapagos | SEEQ40 | 932040EE | 8' | 5'
lali | Ecuador | La Libertad | SEPO40 | 3540B126 | 7' | 5'
sant | Ecuador | SantaCruz,Galapagos | SEEQ40 | 932085F0 | 9' | 5'

## Slide 23: Stations provided by Dirección de Hidrografía y Navegación (Perú) Status at 2022-09-25: 3 stations listed
Code | Country | Location | Connection | DCP ID | Delay | Transmit Interval
atic | Perú | Atico | SEPR40 | 9323727A | 2415d | 1h
call | Perú | Callao,La-Punta | SEPO40 | 354165B4 | 8' | 5'
tala | Perú | Talara | SEPO40 | 35414358 | 8' | 5'

## Slide 24: Stations provided by Dirección General Marítima (Colombia) Status at 2022-09-25: 14 stations listed
Code | Country | Location | Connection | DCP ID | Delay | Transmit Interval
cove | Colombia | Coveñas | ftp |  | 783d | 15'
malp | Colombia | Malpelo | ftp |  | 779d | 15'
sapz | Colombia | Sapzurro | ftp |  | 160d | 5'
buve | Colombia | Buenaventura | ftp |  | 160d | 5'
inav2 | Colombia | Isla Naval | ftp |  | 160d | 5'
tumc | Colombia | Tumaco | ftp |  | 160d | 5'
sama | Colombia | Santa Marta | SEPO40 | 35419530 | 65d | 5'
malp2 | Colombia | Malpelo | SXCO41 | 15AAB424 | 39d | 5'
tumc2 | Colombia | Tumaco | SXCO41 | 15AAC2B4 | 19' | 15'
cart | Colombia | Cartagena | SXCO41 | CB046524 | 13' | 1h
buve2 | Colombia | Buenaventura | SXCO41 | 15AA92C8 | 12' | 5'
inav | Colombia | Isla Naval | SXCO41 | 15A05856 | 9' | 15'
sapz2 | Colombia | Sapzurro | SXCO41 | 15A045F2 | 9' | 5'
sana | Colombia | San Andres | SEPO40 | 35418646 | 8' | 5'

## Slide 25
Questions?
Thanks.
www.ioc-sealevelmonitoring.org
info@ioc-sealevelmonitoring.org