## Slide 1
Assess-1: Tsunami Hazard Zones are Mapped
and Designated
Alessandro AMATO, Fabrizio ROMANO
National Institute of Geophysics and Volcanology (INGV)
Tsunami Warning Center (Italy)
Pio DI MANNA
Istituto Superiore per la Protezione e la Ricerca Ambientale (ISPRA)
IOC-UNESCO EU DG ECHO CoastWAVE Project
IOC-UNESCO Tsunami Ready Recognition Programme (TRRP) Workshop
Online, February 16-17, 2023

## Slide 2: IOC-UNESCO Tsunami Ready Recognition Programme (TRRP) Workshop
Ingredients for a recipe to inundation mapping
2
PTHA
Data
Propagation
Inundation
Hazard curves
Disaggregation
Bathymetry
Topography
Friction coeff.
Nonlinear Shallow Water
Boussinesq
NH
Green’s law
Amplification Factors
Bathtub, Attenuation
Energy grade line
Explicit numerical modeling (SW, Navier Stokes 3D )
Tsunami Ready A1 Indicator
The primary source for mapping potential tsunami hazard zones is inundation modelling, which illustrates expected areas to be flooded by the tsunami. The result of an inundation modelling study is the tsunami inundation map depicting the tsunami hazard zone.

## Slide 3
The Italian evacuation and long-term coastal planning
3
Probabilistic Tsunami Hazard Analysis (PTHA)
Different scales
Global
Davies et al., 2018
NEAMTHM18
Basili et al., 2021
Regional
Local
Computational & human resources, accuracy, time, cost

## Slide 4
Different ways to compute/estimate the tsunami inundation
4
Green’s Law
Amplification factors
Energy Grade Line
Bathtub/Attenuation
Numerical modeling
Synolakis, 1991
Kamigaichi, 2014
Lovholt et al., 2012
Glimsdal et al., 2019
Kriebel et al., 2017
Tada et al., 2018
Leonard et al., 2008
Tonini et al., 2021
Gibbons et al., 2022
Increasing complexity
Calibrated Green’s Law
Gailler et al., 2017

## Slide 5
Numerical modeling
Attenuation rule
Level of the analysis for different methods
5
Accuracy & Data resolution (e.g. topo/bathy)
Computational & human resources, time, cost
Level of metrics
GL
AF
Bathtub
Levels depend on available Data and Resources
https://www.fema.gov/flood-maps/products-tools/hazus
Calibrated GL

## Slide 6
The Italian evacuation and long-term coastal planning
Probabilistic Tsunami Hazard Analysis (PTHA)
The Hazard Curves
http://www.tsumaps-neam.eu/
The model uncertainty in each POI is estimated by means of a variety of hazard curves, one for each alternative model obtained by adopting different assumptions, data, parameters, modelling. The distribution of these curves opportunely weighted describes the epistemic uncertainty associated to the hazard model

## Slide 7
The Italian evacuation and long-term coastal planning
7
Regional Hazard (NEAMTHM18)
2500 yr ARP + 84th percentile
Safety factors
Coastal dissipation
DirPC SiAM; DPC, 2018
Alert Levels
Advisory: runup up to 1m
Watch: runup exceeding 1m
From Regional to Local scale
Hazard curves
MIH  Runup max
Runup max  Inundation
Inundation Maps

## Slide 8
The Italian evacuation and long-term coastal planning
8
Regional Hazard (NEAMTHM18)
2500 yr ARP + 84th percentile
Safety factors
Coastal dissipation
DirPC SiAM; DPC, 2018
Alert Levels
Advisory: runup up to 1m
Watch: runup exceeding 1m
From Regional to Local scale
Hazard curves
MIH values at POIs
~2% in 50 yr (design probability)
For inundation we need to switch from MIH at POIs to Max Runup for stretch of coast

## Slide 9
The Italian evacuation and long-term coastal planning
9
Regional Hazard (NEAMTHM18)
2500 yr ARP + 84th percentile
Safety factors
Coastal dissipation
DirPC SiAM; DPC, 2018
Alert Levels
Advisory: runup up to 1m
Watch: runup exceeding 1m
From Regional to Local scale
Hazard curves
MIH  Runup max (Rmax)
From MIH at POIs to Max Runup for stretch of coast
MIH is a mean value in the inland area corresponding to a specific POI  none 2D perspective
Comparison w/ 2D inundation modeling
MIH can be 3-4x larger!!!
Rmax=MIH*3
3 is the safety factor
To account the tsunami variability along the coast, Rmax on the coast is the maximum value within 40 km

## Slide 10
SiAM – Italian Tsunami Early-Warning System
Summary of the presentation
Methodology: GIS approach and empirical rule application
Input data and processing
Results: inundation maps/alert zones
Tsunami Map Viewer: availability and accessibility of inundation maps
Future goals - improving the maps and the methodology
SiAM alert/hazard zones

## Slide 11
We adopted a GIS- based approach following an empirical model of propagation and inundation.
Fraser & Power, 2013
The empirical relationship between run-up and inland wave penetration is based on the filed surveys and observations following recent and historic tsunami events, especially in the Pacific area, in particular that of Tohoku (Japan) in 2011.
Calculation of dry/wet pixels by GIS tools
Following Fraser & Power (2013), a linear attenuation rule between the R (run-up) values and D ( maximum expected inland inundation distance) is applied.
Methodology: empirical approach for inundation maps

## Slide 12
Empirical relationship between run-up and inundation distance
Section (not in scale) shows the definition of the boundary of the alert zones corresponding to the Advisory e Watch levels
R is the calculated design run-up for each coastal sector
D is the maximum expected inundation distance - D(R)
tgα=0.005
f=1/tgα=200
D=R*f
D=R*200
f=1/tgα

## Slide 13
Inundation zones boundary and coastal morphology
This sketch (not in scale) shows the method used to draw inundations maps in different coastal morphology .
Steep morphology - coastal scarp
Flat morphology - coastal plain

## Slide 14
Input data: collected elevation and morphological dataset
DEM tinitaly
Coast Line 2009
Regional DTMs 1-2-5 meters resolution
DEM IGM 20m
River network
ISPRA – 250k (updated at 10.000 scale)
Coast Line 2006
8.300 km in lenght
High resolution LIDAR data
Elevation accuracy up to 15cm

## Slide 15
Input data: mosaicking and the harmonization
DEM tinitaly
DTM 1-2-5-10 meters res.
DEM IGM 20m
High resolution
LIdar data
Elevation accuracy up to 15cm
New mosaicked homogeneous raster covering
the whole potential
inundation area

## Slide 16
Input data: run-up values
MIH from SPTHA (Seismic Probabilistic Tsunami Hazard Analysis),
Regional Hazard Model
The Project provides MIH values for POIs. MIH values have been converted in run-up values for every coastal sector and used for the definition of the evacuation zones

## Slide 17
Attenuation rule application and data processing
river
mouth

## Slide 18
Calculation of dry/wet pixels by GIS tools
river
mouth
Wet pixels necessary conditions:
1) The position of a generic point x is inside the maximum potential inundation area;
2) The elevation of a generic point x is less than or equals to the R value
Raster calculation of dry/wet pixels by GIS tools based on the application of the D=Rf empirical rule
Both the conditions are satisfied for the point p1 only
The blue line is the inundation boundary

## Slide 19
Definition of alert/hazard zones
Combining the run-up values and the related inundation maps we elaborated the alert/evacuation zones for the Italian coastal regions
+
Tsunami hazard model- INGV
Inundations maps - ISPRA
Definition of alert/evacuation zones
based on

## Slide 20
Tsunami Map Viewer – evacuation maps accessibility
The alert zones are available at the link: http://sgi2.isprambiente.it/tsunamimap/

## Slide 21
Tsunami Map Viewer – SiAM alert zones
Watch ---- zone 2
Advisory----zone 1
Single zone
Watch and Advisory
Messina
Messina
Messina
Messina

## Slide 22
Tsunami Map Viewer – SiAM alert zones
Single zone
Watch ---- zone 2
Advisory----zone 1
Watch and Advisory

## Slide 23
Tsunami Map Viewer – information, web services and download

## Slide 24
Tsunami Map Viewer – download
https://sgi.isprambiente.it/tsunamiweb/
Login

## Slide 25
Future goals: improving inundation maps
Availability of new input data
High resolution DTM coverage
Increase of LIDAR data coverage through new acquisition
Updating data on coast line and river network
Detailed coastal bathymetry data
Detailed 3D data on coastal protection works, easy to flow ways, etc.
Progress in the methodology
Use of specific factors as function of the morphology and of the land use
Use of attenuation factors associated with protective structures/barriers
Contextualization of the analyses, considering local conditions (barriers and easy to flow ways, typical in urbanized areas)
Integration with the results of numerical modelling for relevant coastal sectors
Uncertainty estimation improvement
New version and release
based on
The now available SiAM evacuation maps could be considered as a preliminary version, subject to improvement and periodical updates and changes

## Slide 26
What we need for inundation and evacuation maps

## Slide 27
UNESCO
Intergovernmental Oceanographic Commission (IOC)
Questions: alessandro.amato@ingv.it - fabrizio.romano@ingv.it - pio.dimanna@isprambiente.it
IOC-UNESCO DG ECHO CoastWAVE project
UNESCO IOC Sector Tsunami Unit
d.chang-seng@unesco.org
CoastWAVE project website