## Slide 1
Observing the Ocean and Earth with
18th Tsunamis and Other Hazards related to Sea Level Warning and Mitigation Systems (TOWS-WG)
24-25 February 2025,
UNESCO Headquarters, Paris, France
SMART Cables - update
Juanjo Dañobeitia,
IOC-UNESCO Liaison JTF SMART Cables
Bruce M. Howe, Ceci Rodríguez and Jose Barros
JTF SMART Cables Initiative International Programme Office
University Hawai'i at Mānoa

## Slide 2
United Nations initiative to bring together science with the telecom industry for Global Ocean and Earth Observation
ITU/WMO/UNESCO-IOC JTF SMART Cables
Ocean general circulation – all scales
Climate
Change
Earthquakes and Tsunamis
Sea Level
Rise
Ocean heat and circulation
Disasters Tsunamis Mitigation
Early Warning
Notes: These are the main drivers of this initiative, The SMART data will allow a better understanding of the ocean and the earth.
Water flows from high pressure to low pressure allowing us to see changes in heat content and ocean circulation and sea level rise – key for understanding short and long term climate.
Also allows to see the ocean circulation in a global scale for climate change
It will provide real time data to the operational earthquakes and tsunami warning centers
SMART data will provide a better understanding in the seismic component since there are no seismic motion sensors in the deep ocean, only on land.
Providing early information so their SOP can start earlier than now.
It will also allow to observe the propagation of the tsunami in the ocean to give us a better understanding of the potential threat.

## Slide 3
SMART Cables Governance
Strategic Objectives and Outcomes
Enhanced Climate Monitoring: Use SMART cables to observe ocean heat content, deep ocean circulation, and sea level rise in remote or data-starved areas to improve understanding and mitigate the impacts of climate change.
Improved Disaster Mitigation: Leverage SMART cables to shorten early warning times for tsunamis and earthquakes in real time, reducing risks to coastal communities.
Global Coordination and Standards: Establish SMART cables as a global standard for ocean observation through collaboration with GOOS and ITU standards.
Capacity Building: Support sustainable development and foster global participation through training, partnerships, and equitable resource distribution.
Objective: To explore the feasibility of widespread deployment of scientific instrumentation on ocean telecom fiber-optic cables to enhance capabilities for climate monitoring, tsunami detection, and disaster mitigation. streams as go live
By integrating strong governance, targeted research and development, and global collaboration, this initiative aims to establish a SMART-enabled submarine cables network to address critical ocean sustainability and resilience challenges. This initiative is supported by coordination with three UN sponsoring agencies: ITU, WMO and UNESCO-IOC.
Notes: These are the main drivers of this initiative, The SMART data will allow a better understanding of the ocean and the earth.
Water flows from high pressure to low pressure allowing us to see changes in heat content and ocean circulation and sea level rise – key for understanding short and long term climate.
Also allows to see the ocean circulation in a global scale for climate change
It will provide real time data to the operational earthquakes and tsunami warning centers
SMART data will provide a better understanding in the seismic component since there are no seismic motion sensors in the deep ocean, only on land.
Providing early information so their SOP can start earlier than now.
It will also allow to observe the propagation of the tsunami in the ocean to give us a better understanding of the potential threat.

## Slide 4
SMART Technical Solution
Sensors:
Temperature
Pressure
Seismic
Key point:
Essential Ocean Variables
Shared Cable Infrastructure: Telecom + Science
Sketch of the deployed technological system
Leverage Existing Technology
Guralp and Global Marine
InSea Wet Demo seabed sensor module at Western Ionian Facility (INGV-EMSO)
SMART Cable location off Catania, Italy
Notes: These are the main drivers of this initiative, The SMART data will allow a better understanding of the ocean and the earth.
Water flows from high pressure to low pressure allowing us to see changes in heat content and ocean circulation and sea level rise – key for understanding short and long term climate.
Also allows to see the ocean circulation in a global scale for climate change
It will provide real time data to the operational earthquakes and tsunami warning centers
SMART data will provide a better understanding in the seismic component since there are no seismic motion sensors in the deep ocean, only on land.
Providing early information so their SOP can start earlier than now.
It will also allow to observe the propagation of the tsunami in the ocean to give us a better understanding of the potential threat.

## Slide 5
3700 km, ~20 SMART ASN CC modules +DAS fiber
Gov’t €154M. EU support €56M
SMART 15% ➔ €22M ~ €2/citizen/25 y
~= 2 Tsunami buoys, 25 year (unreliable,
no seismic, not real time)
Lisbon
Azores
Madeira
Portugal SMART Atlantic CAM
450 km long, 4 SMART CC nodes, 2 DAS
Data Center, Scientific Research
France funding €18M SMART (telecom: AFD, ADB)
TAMTAM SMART Cable System
25+ year life, reliable, low lifetime cost
Leverage $5B/y industry, 170 y
SMART Cable Systems
Notes: We do this with the SMART contribution. The Repeaters of the cable systems will have Sensors that will measure ocean bottom temperature, pressure, and seismic acceleration.
Sensors can be mounted in or connected to the repeaters of a telecom cable for power and communications, approximately every 70 km.
Considering a Telecom system lifetime is 25 years with minimal maintenance, adding these sensors can transform the “deaf, dumb, and blind” cables
to environmentally aware systems and thereby improve their integrity and resilience.
Alcatel Submarine Networks, the largest supplier of submarine telecom systems, is very publically committed to supplying SMART capability in the 2025 timeframe as part of its “Climate Change Solution” – a good example of the Blue Economy in action.

## Slide 6: North Atlantic & Polar (Arctic & Antarctica) Systems
Polar Connect Far North Fiber and neighboring Atlantic Projects (Tussas, PISCES, IRIS, IOMEA, etc.
Antarctica Chile
AUS/NZ Antarctica
(NSF MacMurdo)
Notes: We do this with the SMART contribution. The Repeaters of the cable systems will have Sensors that will measure ocean bottom temperature, pressure, and seismic acceleration.
Sensors can be mounted in or connected to the repeaters of a telecom cable for power and communications, approximately every 70 km.
Considering a Telecom system lifetime is 25 years with minimal maintenance, adding these sensors can transform the “deaf, dumb, and blind” cables
to environmentally aware systems and thereby improve their integrity and resilience.
Alcatel Submarine Networks, the largest supplier of submarine telecom systems, is very publically committed to supplying SMART capability in the 2025 timeframe as part of its “Climate Change Solution” – a good example of the Blue Economy in action.

## Slide 7
Pacific, Mediterranean, Indian Oceans
NZ - Chathams
Indonesia
Galapagos
Medusa
MISTS
50 km, 2 module test system installed off Labuan Bajo
Barracuda

## Slide 8
Scientific benefits
Global ocean warming and acidification
Impact and sustainability of Marine Resources exploitation
Real-time observations and early warning systems for earthquakes & tsunamis
Marine Ecosystems and Climate Change mitigation
Earth interactions hydrosphere, biosphere,
lithosphere, atmosphere
Global Array: Climate, Oceans, Sea Level, Earthquakes, Tsunamis
  To enhance Ocean Global monitoring by integrating sensors into submarine telecommunications cables
  To establish a robust SMART Cable network by strengthening cooperation between research infrastructures, providing its DOOS deep-sea component, and fully integrating into GOOS
  To improve Tsunami and Earthquake detection and early warning systems.
  Encourage technology innovation and development, enhancing cooperation with telecom, industry, and science
  To gain a better knowledge of the complex processes within water column, seafloor and sub-seafloor
  To assess the crucial role and evolution that these processes play in the Earth dynamic systems, as global changes, ocean acidification, geological hazards

## Slide 9
Concluding Remarks
Create a Planetary sensor, power, Internet network
Global Array: Climate, Oceans, Sea Level, Earthquakes, Tsunamis
SMART – coupling with telecom – connectivity, climate, DRR – three for the price of one – saves on all fronts
Anticipated additional 1.3 Gm of cable in water by 2037
Leverage annual investment ~ $ 5 Billion
25+ year life, highly reliable, low lifetime cost
Recent successes – set precedents for future systems
Challenges: $, tech, data, legal, regulatory, security, …
EU Funding: Cables w/ SMART
Working with GOOS, Tsunami, Ocean Decade, DOOS, RENs
SMART Cables was endorsed by ODTP, and TOWS
Think globally, act locally!
Good opportunity for countries to lead!
Still much to achieve
Saving Lives

## Slide 10
Scan to Join!
ITU/WMO/UNESCO IOC Joint Task Force
SMARTCables.org
18th Tsunamis and Other Hazards related to Sea Level Warning and Mitigation Systems (TOWS-WG)
24-25 February 2025,
UNESCO Headquarters, 75007 Paris, France