## Slide 1: Overview and Summary of Existing Sensors in the context of UN ODTP forecasting targets
9th Joint ICG/PTWS–IUGG/JTC Workshop 60th Anniversary of the ICG/PTWS – Past and Future, Part II 7th April 2025, Beijing, China
A Moseley | Co-Director, Joint Australian Tsunami Warning Centre

## Slide 2: UN ODTP, 2021-2030 Forecasting Targets
Target forecasting goals from the 10-year Research, Development and Implementation Plan of the UN ODTP.
Notes: In this presentation I’ve included only stations which are open and available in real-time.
This represents the minimum available data for a Regional Tsunami Service Provider.
Of course, some TSPs, may have access to additional stations from private networks – e.g. from their national networks (if not already open), and/or via direct data-sharing/access arrangements with a station operator in another country.
So, in short, some TSPs will have more data than this in some regions. Others may not. This represents the baseline monitoring/observing capability, today.
For the purpose of this analysis, I’ve assumed stations are online and data latencies are small.
Data we’ve
SAGE: Seismological Faciltity for the Advancement of Geoscience, operated by Earthscope --- formerly IRIS
IGS: International GNSS Servics, a service of the International Association of Geodiesy, its Global Geodetic observing system (GGOS), the International Union of Geodesy & … more than 500 GNSS stations.
GOOS: IOC-led Global Ocean Observing System sponsored by WMO, UN Environment Programme and International Science Council (GLOSS: 290 tide gauges;

## Slide 3: Current observing technologies
Open, real-time data – TSP baseline capability
Sources:
  Earthscope SAGE (seismic);
  IAG IGS (GNSS);
  GLOSS (sea-level)
Notes: In this presentation I’ve included only stations which are open and available in real-time.
This represents the minimum available data for a Regional Tsunami Service Provider.
SAGE: Seismological Faciltity for the Advancement of Geoscience, operated by Earthscope --- formerly IRIS
IGS: International GNSS Servics, a service of the International Association of Geodiesy, its Global Geodetic observing system (GGOS), the International Union of Geodesy & … more than 500 GNSS stations.
GOOS: IOC-led Global Ocean Observing System sponsored by WMO, UN Environment Programme and International Science Council (GLOSS: 290 tide gauges;
Of course, some TSPs, may have access to additional stations from private networks – e.g. from their national networks (if not already open), and/or via direct data-sharing/access arrangements with a station operator in another country.
So, in short, some TSPs will have more data than this in some regions. Others may not. This represents the baseline monitoring/observing capability, today.

## Slide 4: SAGE: seismic (broadband, open, real-time)

## Slide 5: IGS: GNSS stations (open, real-time)

## Slide 6: GOOS: tide & DART (open, real-time)

## Slide 7: GOOS: DART (open, real-time)

## Slide 8: Seismic + GNSS + DART + Tide gauges

## Slide 9: Earthquake source

## Slide 10: Earthquake: initial indicators, OT+3’
Notes: A1, Initial Indicators: earthquake - initial location & magnitude [ML, Mwp?]
Method: discretised source zones into 50km points. Allowing for 20s data latency
  Requiring 6 stations within ~20deg.
  No constraints on azimuthal coverage
Expect: low quality solution: useable location (assume shallow), very unreliable magnitude (ML, Mwp? mb) (assume underestimated); some first motions (assume thrust)

## Slide 11: Earthquake: initial indicators, OT+3’
Notes: A1, Initial Indicators: earthquake - initial location & magnitude [ML, Mwp?]
Method: discretised source zones into 50km points. Allowing for 20s data latency
  Requiring 6 stations within ~20deg.
  No constraints on azimuthal coverage
Expect: low quality solution: useable location (assume shallow), very unreliable magnitude (ML, Mwp? mb) (assume underestimated); some first motions (assume thrust)

## Slide 12: Earthquake: source partially constrained, OT+10’
Notes: A2 W-phase window is S-P, so at ~9minutes, S roughly 25degrees. But, first-motion mechs, if you want to include them, can be done on P making it ~60 degrees. So, choice, wphase (accepted standard for forecasting) or enough to make a perhaps dubious estimate?
A2, Partially constrained:
  Requiring 20 stations within ~60deg [P-arrival];
  Max AzGap <180deg
  S out to ~25deg (no constraint on AzGap for wphase)
  Expect: Mww, centroid, possibly some FM from P-arrivals (assume vertical motion). Acceptable standard for forecasting?

## Slide 13: Earthquake: source fully constrained, OT+45’
Notes: A3, fully constrained:
  Requiring wphase + 1 DART or 2 DARTS
  Expect: [orange] at least good quality wphase (OT+45);
    [green] also confirmation of tsunami with 1 or more wave-height observations for scaling forecast.

## Slide 14: Earthquake: source fully constrained, OT+45’
Notes: A3, fully constrained:
  Requiring wphase + 1 DART or 2 DARTS
  Expect: [orange] at least good quality wphase (OT+45);
    [green] also confirmation of tsunami with 1 or more wave-height observations for scaling forecast.

## Slide 15: Non-earthquake, known source

## Slide 16: Non earthquake (known): initial indicators, OT+10’
Notes: B1 Needs something to localise source AND 1 dart. So, seismic info plus 1 dart. Assume Seismic info is P onset -> 20 degrees, seismic, 1 DART
B1, Initial Indicators: volcano or secondary source (landslide from earthquake)
  Assuming source can be localised from:
    seismic (P-onset): require 6 stations within ~20deg or from
    GNSS (2 stations within 200km) – 200km radius; station separation 100km+
    PLUS + 1 DART.
  Expect: useable location [if you can see it!], wave-height for confirmation (and scaling?)

## Slide 17: Non earthquake (known): partially constrained, OT+45’
Notes: B2 – at least, localisation and 2 DARTs. In practice, the DARTs would have to sample the beam propagating toward the forecasted coast.

## Slide 18: Non earthquake (known): fully constrained, OT+60’
Notes: B2 – at least, localisation and 2 DARTs. In practice, the DARTs would have to sample the beam propagating toward the forecasted coast.

## Slide 19: Non-earthquake, unknown source

## Slide 20: GOOS: tide & DART (open, real-time)

## Slide 21: Summary – progress against UN ODTP
OD mid-point…
Currently available data is not enough to achieve UN ODTP forecasting targets.
New infrastructure slow to come into effect (e.g., SMART) – and will data be open?
Large-scale infrastructure investment for ocean observations, not expected.
Necessary next steps:
  Increase open data sharing from existing stations
  Look to other existing ocean-observing technologies and novel techniques to augment existing capability – e.g., GNSS-TEC, Satellite altimetry, OF interferometry, others?
  Collaborate with researches to make novel data forecast-ready for TSPs
  Partner with those operators/sectors to access novel data (ad hoc or continuous).