## Slide 1
Hyderabad, India
FIRST CONFERENCE OF THE OCEAN DECADE TSUNAMI PROGRAMME
10-11 November 2025
Landslide tsunami hazards
Finn Løvholt1,2,3
Carl Harbitz1,2,3, Sylfest Glimsdal1,2,3
1 - Global Tsunami Model (GTM)
2 - Norwegian Geotechnical Institute (NGI)
3 – International Centre for Geohazards (ICG)

## Slide 2: Landslide tsunamis
Landslide and rock avalanche tsunamis - roughly 10-15% of the reported tsunami sources globally
(Harbitz et al., 2014, Nat Haz)
Two main classes of landslides
  Submarine landslides
  Subaerial landslides, including volcano flank collapses
Can in principle occur on any slope
  Seismically passive or active margins
More local character than earthquake tsunamis, with potentially severe impact
More complex generation and progatation process than earthquakes
Map showing landslide tsunamis, volcanic tsunamis, and joint earthquake/landslide tsunami events
Source, NCEI, NGDC, NOAA

## Slide 3: Submarine landslides and tsunamis around the globe
1998 PNG tsunami - Image courtesy of Jose Borrero
> 2 000 fatalities
1929 Grand banks tsunami – Løvholt et al., (2019), GSL
> 300 km3 – 27 Fatalities in Newfoundland
Gulf of Cadiz database, Zengaffinen-Morris et al., (2022), JGR
Hühnerbach et al., (2004), Mar Geol
US East Coast database
Lee (2009), Mar Geol
Heterogeneously mapped globally
Many events back far back in time, dating often uncertain
A very small fraction of the mapped events are tsunamigenic
Most major landslides pre-historical

## Slide 4: Subaerial landslides tsunamis More frequent, more local, high local impact
Year | Event | Country | Volume | Max run-up
2000 | Paatuut | Greenland | ~50 Mm3 | > 50 m
2002 | Stromboli (two slides) | Italy | 4-9 Mm3 and 20 Mm3 | > 10 m
2003 | Qianjiangping | China | 24 Mm3 | 39 m
2007 | Dayantang | China | 3Mm3 | ~50 m
2007 | Aysen fjord | Chile | High number of slides | ~50 m
2008 | Chehalis Lake | Canada | 3Mm3 | 38 m
2008 | Three Gauges | China | 0.38 Mm3 | 13 m
2014 | Lake Askja | Iceland | ~20 Mm3 | 80 m
2015 | Icy Bay | USA | 76 Mm3 | 193 m
2017 | Karrat fjord | Greenland | ~40 Mm3 | 90 m
2018 | Bureya | Russia | 25 Mm3 | 90 m
2018 | Baige | China | >10 Mm3 | 54 m
2018 | Anak Krakatau | Indonesia | ~210 Mm3 | 85 m
2020 | Elliot Creek | Canada | 13.5 Mm3 | 120 m
2023 | Dickson fjord | Greenland | 25 Mm3 | 200 m
2025 | Tracy Arm | Alaska | ~100 Mm3 | >30 m
2015 Taan fjord / Icy Bay
Courtesy C Larsen
Selected events since year 2000
43 m
56 m
76 m
Lake Askja 2014
Courtesy IMO
2007 Aysen fjord
Courtesy H Fritz, GA Tech
2023 Dickson fjord
Svennevig et al., 2024 - Science
Global seismic signal from seiche

## Slide 5: Generation mechanisms
8000 BP Storegga slide and tsunami
(Courtesy, S. Gibbons, NGI)
2014 Lake Askja slide and tsunami
(Courtesy, M. Rauter)

## Slide 6: Landslide tsunami characteristics and modelling needs
Main factors of importance for the generation
  Submarine landslides: water depth, slope, rheology
  Subaerial landslides: impact area and velocity
Models need to provide time dependent slide motion
  Capturing rheological properties of the landslide
  Include effect of ambient water
  Linking landslide and tsunami models
Wave shapes and propagation differs from earthquakes tsunamis
  Higher amplitudes, shorter length and aspect ratio, frequency dispersion
  Needs more sophisticated models than SWE, e.g.:Boussinesq, layered models, CFD
Frequency dispersion
PNG – slump - dipole
(Lynett et al., 2003,
PAGEOPH)
Landslide rheology and dynamics
Løvholt et al., 2015, Royal Soc
Rauter et al., 2022,
Nature Comm
Clay material
Particle dominated

## Slide 7: We still need to advance the way we test and improve our prediction models
For idealized studies, physics, model consistency
  NTHMP benchmark tests
  Mainly laboratory tests
  https://www1.udel.edu/kirby/landslide/
Testing towards field events
  Tsunami generation does not scale from lab to field
  Calibration of hazard model
  USGS/USC led initiative – validation towards Taan fjord – revealed need for improvement
  A range of the most recent well documented events can be also used (e.g. Greenland, Alaska, Norway, Iceland)
Lake Askja 2014, Rauter et al., 2022, Nature Comm
2015 Taan fjord
Courtesy C Larsen
  NTMHP Benchmark tests - examples
Friction depends on the volume,
Lucas et al., 2014, Nature Comm

## Slide 8: Landslide Probabilistic Tsunami Hazard Assessment (LPTHA)
Estimating tsunami probability of occurrence
Two alternative pathways to anchor probabilities
- Basis on past landslide data
- Based on slope stability
LPTHA can largely mimic PTHA for earthquakes:
Generate a synthetic set of sources
Define annual source probabilities
Simulate the wave propagation for each source
Aggregate probabilities from all simulations to hazard curves
Tsunami simulation
Landslide statistics, frequency
Hazard
curves
Landslide databases

## Slide 9: We have only a few extensive hazard applications
Cook Strait Canyon, NZ
(Lane et al. 2016, PAGEOPH)
  Submarine landslides
  Simplified landslide dynamics
  Well constrained geological setting and timing
Lyngen fjord Northern Norway
(Løvholt et al. 2020, Landslides)
  Subaerial landslides
  Four unstable slopes
  Probabilities from rock slope stability analysis (subjectively established)
  Uncertainty treatment of generation mechanisms (velocity and impact area)
In both cases, model calibration needed

## Slide 10: The Norwegian system – an example of early warning and hazard analysis for local communities
Link between tsunami hazard model and early warning system
Rock slope monitoring using a variety of fit for purpose instrumentation systems e.g.
  Boreholes, extensometers
  InSAR
  GPS
  Microseisms
Slope motion mirrored into regional hazards models
Early warning issued a minimum of 72 hours in advance of slide release
Courtesy:
Lene Kristensen NVE
Identified slopes
Monitored slopes
Some near water bodies
Borehole measurements
InSAR
GPS station

## Slide 11: Scaling up: Challenges related to hazard, risk analysis, early warning
Statistical background often lacking, limited, or lacks dating
Data on slope information limited or non-existing
  Difficult to constrain volumes and probability
  Acquiring data often expensive, and limited to local investigations
More local nature of landslides makes them more difficult to survey
They are not necessarily linked to triggers or precursors – and travel times can be short
 Warning times based on wave measurements may be too short
Stromboli wave recording
Ripepe and Lacanna (2024), Nature Comm
Zengaffinen-Morris et al. (2022), JGR Oceans

## Slide 12: Some final reflections
Landslide tsunamis recognized as an important source for tsunami hazards
Tsunami hazard models less developed, partly because of lack of data
New hazard models will depend on data, either past landslide statistics or slope stability data and models – without it we cannot quantify return periods (only conditional hazard)
With respect to early warning for all, landslide tsunamis constitute a major challenge:
  There are few systems today (Norway and Stromboli perhaps the only ones)
  Landslide tsunamis are highly local
  Wave signature different from earthquakes, and difficult to test as data is lacking
  Need for instrumentation extensive and expensive – regional efforts might become infeasible at present
  Most effective for areas with known hazard / slope instability

## Slide 13: Extra slides

## Slide 14: Outstanding questions and gaps – the GTM community response from 2021
Gap 1: Understanding and quantifying landslide volume probability
Gap 2: The difference in tsunami genesis – from onshore to offshore
Gap 3: Lack of constrains on landslide dynamics
Gap 4: Lack of available benchmark tests
Gap 5: Limited past events to inform hazard models
Gap 6: Lack of ability to accurately model tsunami generation
Many of the landslide related gaps rank high
In particular landslide probability highest but also most difficult
Importance
Difficulty to achieve
G1
G3
G5
G2
G4
G6

## Slide 15: Submarine landslide tsunami generation
Quadrupole shape –
Storegga slide
Mechanism: Water volume displaced by landslide
  Time dependent, the motion of the landslide matters
Wave shapes differs from earthquake tsunamis
  Dipole or quadrupole shape – different aspect ratio
  Shorter wave-length
Main factors of importance
  Water depth – shallow events more tsunamigenic
  Slope – higher acceleration and velocity increases the tsunami-genesis
Drawdown
Elevation
Basic generation mechanism from submarine landslide
Frequency dispersion
PNG – slump - dipole
(Lynett et al., 2003)

## Slide 16: Subaerial landslide tsunami generation
Generation mainly due to the surface impact
Extensively studied in laboratory – numerous papers (likely more than 100 studies)
Wide range of source mechanisms and geometric settings
  Various scaling expressions in literature
  No consensus model
Parametric scaling relationships – main parameters:
  Impact velocity
  Frontal area
Bullard et al., (2019)
Review of impact tsunamis studies:
Heller and Ruffini (2023), ESR
Many studies, but heterogeneous outputs

## Slide 17: Landslide and tsunami models must be combined for optimal predictions
Landslide dynamics models
  Clay dominated: Cohesive fluid dynamics models
  Particle interaction dominated, sand / rock: Frictional collisional fluid dynamics models
  Hydrodynamic resistance / interaction, erosion, entrainment
Coupling (from seabed to wave generation)
Tsunami propagation model needs
  High order dispersion most often needed, e.g. Boussinesq models, layered models, or full 3D models
  Subaerial slides – rock avalanches – hydrodynamic cratering
  Demanding models – need for some compromise for feasibility for e.g. hazard studies
Submarine clay dominated slide
Effects of granular collisions on dynamics
Impact and generation