## Slide 1
Monitoring
high-frequency
sea level fluctuations in coastal regions of Ukraine
Alexander Matygin
Natalia Iakovleva
Hydrometeorological Center
for Black and Azov Seas
Odessa,
Ukraine
Hyderabad, India
FIRST CONFERENCE OF THE OCEAN DECADE TSUNAMI PROGRAMME
10-11 November 2025

## Slide 2
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Tsunamis and meteotsunamis are relatively rare in the Black Sea. Meteotsunamis have been recorded three times in the Black and Azov Seas over the past 20 years.
The Hydrometeorological Service needs to conduct appropriate observations to assess the impact of tsunamis on coastal infrastructure.
These observations should ensure high-quality recording of sea level fluctuation parameters.
Meteotsunami studies should also include recording certain meteorological parameters.
The purpose of the message: the state of hydrometeorological monitoring of the Ukrainian part of the northwestern part of the Black Sea

## Slide 3
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
In accordance with the frequencies (periods) of meteotsunami (tsunami) wave oscillations, it is necessary to record sea and atmospheric parameters with the following resolution:
1 - sea level, resolution every 30 s;
2 - atmospheric pressure (high-frequency fluctuations of 2-6 hPa/5 min) - resolution every 1 min;
3 - wind speed vector, resolution every 1 hour;
4 - aerological parameters of the atmosphere, once daily (wind distribution by height, unstable layers, Richardson number).
*by Rabinovich, Sepic

## Slide 4
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Areas shaded in red represent parts of the sea for which the Froude number is close to unity (0.9\Fr\1.1)
Modified from Sˇepic´ et al.
Areas shaded in red represent
parts of the sea for which the Froude
number
Is close to unity (0.9\Fr\1.1)
Modified from Sˇepic´ et al.
Mediterranean regions
Where meteotsunamis
may occur are highlighted
in red

## Slide 5
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Azov Sea
Odessa
Bulgaria
Meteotsunamis of Black and Azov Seas
Bulgaria 07/05/2007 3
Region Data Wave height, m
Odessa 26/06/2014 3
Azov Sea 19/07/1017 1.5
Black@Azov Sea
The areas
of the Black
and Azov Seas
where meteotsunamis
were observed,
as well as the maximum
heights
of the meteotsunami
waves,
are shown.

## Slide 6
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Six hydrometeorological stations
are located on the Ukrainian coast
of the northwestern Black Sea.
Only two of them are equipped with tide gauges,
But the meteorological equipment
can record changes
in atmospheric pressure and wind
with a resolution of 30 seconds.
The location
of the hydrometeorological stations
allows for the recording of localized
meteotsunami waves
along almost the entire coast.

## Slide 7
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Currently, Ukraine lacks the capacity to fully implement a marine environmental monitoring system (although atmospheric processes are monitored fairly comprehensively, with the exception of aerorological observations due to military actions).
We'd like to make use of Croatia's experience. Meteotsunamis occur quite frequently in this country. Assistance to Ukraine could be provided through the European Twinning and EU4GRE programs.
Ukraine will establish the sea level fluctuation monitoring system to obtain information on processes in the tsunami frequency range.

## Slide 8
First Conference of the
Ocean Decade Tsunami Programme
10-11 November 2025
INCOIS, Hyderabad, India
Thank you for your attention