## Slide 1: Tsunami Detection on Standard Telecommunication Cables
M. Mazur(1), N. K. Fontaine(1), R. Ryf(1), M. Karrenbach(2),
K. L. McLaughlin(3), B. J. Sperry(3), A. G. Butler(3), V. Kamalov(4), L. Dallachiesa(1), E. Burrows(1), D. Winter(1), H. Chen(1), J. Naik(5), K. Padmaraju(5), A. Mistry(5) and D. T. Neilson(1)
(1) Nokia Bell Labs, 600 Mountain Ave, Murray Hill, NJ 07974, USA
(2) Seismics Unusual LLC, Brea, CA 92821, USA
(3) Leidos Inc., Arlington, VA 22203, USA
(4) Valey Kamalov LLC, Gainesville, FL 32607, USA
(5) Nokia Advanced Optics, 171 Madison Ave, New York City, NY 10016, USA
mikael.mazur@nokia-bell-labs.com

## Slide 2
Global Earthquake and Tsunami Warning
Insufficient offshore
Today's global monitoring and warning system
  >>1000 Land-based seismic stations (e.g., Global Seismic Network)
  DART buoys with bottom pressure sensors
  Dedicated tsunami warning cable arrays (S-Net, DONET 1&2)
Challenge: Increase global coverage
  Most of the deep ocean remains unmonitored
  DART buoy coverage sparse (<100 points globally)
  Continuous, real-time, monitoring required for any sensor (<1s latency)
Is there a path to build out global connectivity and early warning together?
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
https://nctr.pmel.noaa.gov/Dart/

## Slide 3
Telecom Submarine Cables
Internet Backbone network, ~1.5 million km globally
www.submarinecablemap.com (19-10-2025)

## Slide 4
Tsunami Detection using Subsea Cables
Dedicated cable-based observatories
  Expensive, custom-made deployment
  Point-based pressure and seismic sensors
  S-Net, DONET 1&2, scientific ocean monitoring cables
Science Monitoring and Reliable Telecommunications (SMART)
  Hybrid cable: telecom and point-based sensors
  First cable expected 2027 (Atlantic CAM in Portugal)
Fiber sensing
  Existing and future telecom cables
  Telecom fibers as distributed strain sensors
  Can be part of future SMART and dedicated cables
M. Mochizuki et. al., S-net project:…, OCEANS, 2018
Portugal Atlantic CAM project: : 22-PT-DIG-Atlantic CAM
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 5
Fiber Sensing
Detecting tsunami waves
  Change in water pressure changes cable length
  Turn telecom fibers into distributed strain sensors
  Can co-exist with telecom traffic (if properly engineered)
Distributed acoustic sensing (DAS)
  High spatial resolution and sampling rate
  Tsunami detection shown near shore
  Limited reach up until first repeater (~50km)
Fiber sensing as a compliment for tsunami detection
  Overcoming reach limitation foundational
T. Tonegava and E. Araki, GRL, 51 (11), 2024
L. Moeller, arXiv: 2304.06905, 2023
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 6
Experimental Setup
Submarine cable: California --- Hawaii
  About 4400km long, ~100 optical repeaters
  First repeater ~35km offshore
  High-loss loopback couplers ~40dB loss
  >4200km at water depths exceeding 4000m
Bell Labs Long-Reach Fiber Sensing
  Supports distances exceeding 10000km
  Compatible with live traffic
  Based on optical frequency domain reflectometry
Intensity measurement
  Single trace, ~1s averaging
  SNR varies between 15 and 5dB
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
HI
CA
~4400km

## Slide 7
M8.8 Megathrust Earthquake
July 29th 2025
Kamchatka Peninsula, Eastern Russia
  Frequent fault for large-scale earthquakes and tsunamis
  6th largest recorded earthquake to date
  Tsunami-generating event
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
https://earthquake.usgs.gov/earthquakes/eventpage/us6000qw60/executive
A. Ruiz-Angulo et. al., https://eartharxiv.org/repository/view/10335/

## Slide 8
M8.8 Mega-Thrust Earthquake
First span
Regular DAS reach limit
P-wave
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
First Span
100m resolution

## Slide 9
M8.8 Mega-Thrust Earthquake
P-wave
Regular DAS reach limit
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
First Span
100m resolution

## Slide 10
M8.8 Mega-Thrust Earthquake
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
First Span
100m resolution

## Slide 11
M8.8 Mega-Thrust Earthquake
All the spans
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
All the spans 4400km
100m resolution

## Slide 12
M8.8 Mega-Thrust Earthquake
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
Near shore
Deep Ocean

## Slide 13
M8.8 Mega-Thrust Earthquake
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
u
u
Earthquake Spectrograms

## Slide 14
https://nctr.pmel.noaa.gov/kamchatka20250729/

## Slide 15
Tsunami Observation
NOAA reference data
MOST (Method of Splitting Tsunami) model
DART Buoy's offshore HI and CA
https://nctr.pmel.noaa.gov/kamchatka20250729/
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 16
Tsunami
DART is close to shore
Fiber sensing enables deep-ocean tracking
DART
Fiber Sensing, 500km offshore Hawaii
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
https://nctr.pmel.noaa.gov/kamchatka20250729/

## Slide 17
Tsunami Monitoring
500km offshore California, >4000m depth
15km offshore California, ~30m depth
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 18
Tsunami Monitoring
1500km offshore California, >4000m depth
1000km offshore California, >4000m depth
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 19
Tsunami Monitoring
2500km offshore California, >4000m depth
2000km offshore California, >4000m depth
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 20
Tsunami Monitoring
50km offshore Hawaii, >1000m depth
500km offshore Hawaii, >4000m depth
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 21
Tsunami Heading for California
Bandpass: 100uHz - 50mHz
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025

## Slide 22
Tsunami
First Fiber-Optic Deep-Ocean Tracking
500km offshore Hawaii
500km offshore California
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
https://nctr.pmel.noaa.gov/kamchatka20250729/

## Slide 23
Conclusions
Earthquake and Tsunami observation
Demonstrated high-resolution distributed acoustic sensing
  ~100m spatial resolution
  44,000 measurement points
  Largest coherent detection array to date
  Compatible with all installed submarine cables
Detection of the M8.8 mega-trust earthquake
  P-, S- and several other phases clearly visible
  Unprecedented spatial resolution on the ocean floor
Demonstrated detection of a tsunami in the deep ocean
  Continuous tracking along the entire cable
  Proves the ability for telecom cables to track tsunamis
M. Mazur et. al., Submarine Cable Deep-Ocean Observation of Mega-Thrust Earthquake and Tsunami with 44,000 100-m Spaced Sensors, 2025
Tsunami 500km offshore Hawaii, >4000m depth