## Slide 1
IPMA National Tsunami Warning Center and TSP - Status
Fernando Carrilho
ICG/NEAMTWS, Paris
03-05 December 2025

## Slide 2: PT.NTWC
Subscribers:
NTWC – November 2017
CTSP - January 2018
Accreditation as TSP on 2019
Portugal, Spain, France, Morocco, Germany, UK, Denmark, Turkey, Italy and Greece
JRC, IOC, ERCC

## Slide 3: Seismic Network
VSAT
Internet
MPLS
VSAT
Internet
IPMA broadband network (+ SM sensors co-located)
IPMA short-period network (+ SM sensors co-located)
IPMA/IST strong-motion network
Real-time, Internet (mobile, mini-link, fiber optic) & VSAT connection
Complemented with stations from other agencies: Portugal, Spain, Morocco, France and CTBTO (Internet, VPN and MPLS);
83 Broadband, 28 short-period and 97 accelerometers (real-time)
Broadband / Short-period
Strong-motion

## Slide 4: Seismic Network – NEW real time DAS
Example of a 1.8ML
60 to 90Km from the cable
- 57Km DAS
- virtual stations each 2km
- downsampled to 125Hz

## Slide 5
SeiscomP – Global Seismic Monitoring
Fast locations
Fast MW evaluations

## Slide 6
Seismic Monitoring
IPMA Automatic solutions
Other agencies solutions
(hypocenters/Mags/MT)

## Slide 7
Seismic Monitoring
IPMA Automatic Mw & CMT
W-Phase method
Implemented on Seiscomp
in late Feb 2023
Contribution:
(Luis Rivera & Anthony Jamelot)

## Slide 8
Tide-gauge network
Internet
MPLS
Internet
MPLS
Instituto Hidrográfico
Direção Geral do Território
JRC (ipma & ign support)
Puertos Del Estado (via IOC & IGN)
CNRST (via CNRST & JRC)
IOC
71 stations
Sources:
CENALT, seiscomp/MPLS (SHAUM stations)
IH, webservice/Internet (Instituto Hidrográfico)
JRC, webservice/Internet
EMSO-PT/UBI/IPMA, webservice/Internet
DGT sites, webservice/Internet (Direção geral do Território)
IGN seiscomp/Internet (Puertos del Estado stations)
El Jadida

## Slide 9
EMSO-PT
MultiParameter Stations
Porto Covo
Arrifana
Porto Santo
Albufeira
Portimão
GNSS
Tide-Gauge
Meteo
Atmospheric Pressure
Temperature
Humidity
Wind
University of Beira Interior
Instituto Português do Mar e Atmosfera
Porto Moniz
Solar Power
Mobile Internet
Local buffer

## Slide 10
Tide-gauge data acquisition
and management
IOC dataservice
JRC
dataservice
DGT
sites
IH
dataservice
IGN
seiscomp
EMSO-PT/UBI/IPMA
ftp
CENALT
seiscomp
TREMOR01
Seiscomp
MareFromWeb

## Slide 11
Decision Matrix

## Slide 12
Forecast coastal segments (national)
Forecast points (regional)
5. Estuário Tejo
6. Setúbal
7. Beja
8. Faro Barlavento
9. Faro Sotavento
Islands
10-11. Madeira & Porto Santo
12-20. Azores islands
Mainland
1. Viana-Braga-Porto
2. Aveiro-Coimbra
3. Leiria
4. Lisboa Atlântico
Regional NEAM level
National level

## Slide 13
TAAR – Tsunami Analysis And Report
Testing purposes
(include random full scenarios)
Exercise Mode
(Neamwave21, others)
Real events and
Communication tests
Internal Exercise Mode

## Slide 14
TAAR – Tsunami Analysis And Report
SMS
EMAIL
FAX
SMS
GTS
EMAIL
FAX

## Slide 15: Regional level – TSP for NE Atlantic
50 Tsunami messages issued:
50 events

## Slide 16
Atlantic SMART CAM
New Submarine Cable Ring connecting PT Mainland-Azores-Madeira –
SMART - Science Monitoring And Reliable Telecommunications - SYSTEM

## Slide 17: SMART CAM – Physical Layout
Carcavelos-Terceira
1 650 km
Total Extention 3,950 km
Sines-Funchal
990 km
Terceira-São Miguel
210 km
São Miguel-Funchal 1,100 km
8 CC nodes
8 CC nodes
4 CC nodes
addapted from ASN
to be operational on the second half of 2027
One of the world’s first “SMART” cables, capable of carrying internet data, but also monitoring the ocean above and the earth below
For an average of 15% increase in cost, four sensors – accelerometer, seismometer, water pressure, and temperature – into the CC Node

## Slide 18: “Tsunami Ready” Initiatives
Cascais
Lisbon
Setúbal
Lagos
Portimão
Loulé
(Lourinhã)
(Sesimbra)
to become
TSUNAMI READY
coastwave 2.0
(National Tsunami
Ready Board Pending)

## Slide 19
Thank you for your attention